## Slide 1
Production
/Attraction Demand
Agent List
Gravity Model
(Auto, Bike, Pedestrian)
Node
Zone
POI
grid2demand: an open-source package to generate zone-to-zone travel demand
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
osm2gmns
osm2gmns
census blocks
TAZs from agencies
Data Sources
Node
Zone from Grid or from TAZ
POI
Package Core Engine
Zone-to-Zone
(OD Demand)
Must include zone_id for activity nodes
trip rate file
Optional

## Slide 2: Current Input Modes Based on Our Meeting (Pls edit the PPT if I misunderstand)

## Slide 3
grid2demand: a tool to generate zone-to-zone travel demand
Input mode 1: Without external zone files (use zone_id in node as activity nodes): Inputs are node and poi
Production
/Attraction Demand
Agent List
Gravity Model
Node
Grid Zone
POI
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
Node
POI
Package Core Engine
Create Grids from nodes
Zone-to-Zone
(OD Demand)
Extract activity nodes from
Node with zone_id content
(Activity nodes)
If activity nodes (zone_id) in node.csv is None, What should we do?
Stop the program!

## Slide 4
Production
/Attraction Demand
Agent List
Zone-to-Zone
(OD Demand)
grid2demand: a tool to generate zone-to-zone travel demand
Input mode 2: with external zone file: (use external zones from TAZs): Inputs are node, zone and poi
Gravity Model
Node
TAZ Zone
POI
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
Node.csv
POI.csv
Package Core Engine
TAZ coded in Zone.csv
census blocks

## Slide 5: Assumptions and Problem Statement
Initial Zone Assignment: In the Chicago dataset example, an initial zone ID for each node is derived from OpenStreetMap (OSM) using the osm2gmns package. The zone ID is initially the same as the node ID.
Activity Nodes: Out of 30K nodes in the Chicago dataset, 3K activity nodes are identified, typically situated on boundary points of primary and secondary streets or interfacing points. Zone IDs assigned by grid2demand are only for activity nodes.
Two Zone System Setup Options:
  Grid Setup: A 10x10 grid is created for the 3K activity nodes. Each activity node assigned to one grid cell.
  External TAZ Setup: Alternatively, 40K census blocks (external TAZ zones) are used, refining zone structures and improving demand pattern capture. Each activity node assigned to external TAZ zone id.
POI-Demand Zone Assignment: The demand for each zone is calculated using proximity-based assignment of points of interest (POIs) within the grid, and sampling (e.g., processing 10% of POIs) optimizes performance. There are about 80K POIs in the Chicago dataset.
Gravity Model for Demand Calculation: A gravity model is used to estimate demand between zones
  1) The production and attraction estimation model should utilize a matrix or vector format to streamline calculations.
  2) For large datasets (e.g., 1M+ POIs), sampling should be implemented, such as using a 10% subset for processing, avoiding the need to scan all POIs.

## Slide 6: Previous Input Modes (grid2demand<= v0.6.4) (I keep these modes for the future tracking)

## Slide 7
Demand
Agent
Zone-to-Zone
(OD Demand)
grid2demand: a tool to generate zone-to-zone travel demand
Mode 1 (create grid zones): Inputs are node and poi
Gravity Model
Node
Zone
POI
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
Node
POI
Package Core Engine
Create Grids from Node
Without zone_id

## Slide 8
Demand
Agent
Zone-to-Zone
(OD Demand)
grid2demand: a tool to generate zone-to-zone travel demand
Mode 2 (use zone_id in node as zone): Inputs are node and poi
Gravity Model
Node
Zone
POI
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
Node
POI
Package Core Engine
Extract zone_id from node as zone
for zone-zone demands
With zone_id

## Slide 9
Demand
Agent
Zone-to-Zone
(OD Demand)
grid2demand: a tool to generate zone-to-zone travel demand
Mode 3 (use external zones from TAZs): Inputs are node and poi
Gravity Model
Node
Zone
POI
Output
Inputs
(bf-processing
Inputs
(sources)
Processing
Node
POI
Package Core Engine
Zone
census blocks